## Slide 1
QNX India Hackathon
Chennai, September 18-19, 2026
LumiGrid-RT
Safety-constrained predictive street lighting on QNX
Four processes. Priority override. Measured behavior.
Notes: Open with the safety problem, then name the project.
This cover is conceptual artwork, not a photograph of the deployed prototype.
Source: Official participant brief supplied by the team. Do not redistribute the source PDF.

## Slide 2
The control gap in current street lighting
100%
Always-on lighting preserves visibility but wastes power during quiet hours.
Reactive
Simple PIR switching responds only after arrival. Independent poles cannot light the path ahead.
Required outcome
Reduce brightness only when daylight, occupancy, expected demand, weather, and sensor health allow it.
Emergency must bypass every energy-saving rule.
02
Notes: Contrast always-on control with purely reactive PIR switching.
The design objective comes from the selected challenge: energy reduction while maintaining safety from traffic and environmental conditions.

## Slide 3
QNX process and message-queue architecture
Critical work stays isolated; the controller owns every lamp decision
Sensor service
FIFO 40
LDR, PIR, visibility
Absolute 250 ms timer
Prediction service
FIFO 30
Controller sensor copy
History + neighbor flow
Emergency service
FIFO 60
Physical or CLI input
Independent timeout
Bounded event queue
Fixed-size messages
Priority 31 emergency
Priority 10 sensor
Lighting controller
FIFO 70
Safety state machine
Latency and energy metrics
Outputs
Zone PWM targets
Status queue
CSV and JSON evidence
03
Notes: Walk from left to right. Emphasize that the predictor never writes PWM directly.
QNX reference: https://www.qnx.com/developers/docs/8.0/com.qnx.doc.neutrino.utilities/topic/m/mqueue.html
The QNX mqueue manager implements POSIX queues, while send and receive use kernel-space queues.

## Slide 4
Deterministic scheduling and priority override
Requested SCHED_FIFO priority
Controller
70
Emergency
60
Sensors
40
Prediction
30
Absolute sensor schedule
t₀
t₀ + 1T
t₀ + 2T
t₀ + 3T
Emergency becomes READY
The emergency service preempts sensor and prediction work. Queue priority 31 moves its event first, then the FIFO-70 controller applies the 100% override.
No cumulative timer drift
04
Notes: Explain READY and BLOCKED in plain language before naming SCHED_FIFO.
QNX FIFO reference: https://www.qnx.com/developers/docs/8.0/com.qnx.doc.neutrino.prog/topic/overview_FIFO_scheduling.html
QNX priority API: https://www.qnx.com/developers/docs/8.0/com.qnx.doc.neutrino.lib_ref/topic/p/pthread_setschedparam.html
QNX absolute timer API: https://www.qnx.com/developers/docs/8.0/com.qnx.doc.neutrino.lib_ref/topic/c/clock_nanosleep.html

## Slide 5
Safety state machine
Daylight prevents wasted activation; emergency and fail-safe remain above it
Priority | State | Trigger | Target
1 | EMERGENCY | Explicit emergency is active | 100%
2 | STARTUP_SAFE | No sensor sample has arrived yet | 70%
3 | SENSOR_FAILSAFE | Sensor is invalid or stale | 70%
4 | DAYLIGHT_OFF | Daylight ≥ 160 lux and no higher state | 0%
5 | ACTIVE | Current or recent PIR activity | 100%
6 | WEATHER_SAFE | Visibility is below the safe threshold | 75%
7 | PRELIGHT | Neighbor activity or probability ≥ 0.65 | 65%
8 | PREDICTIVE | Demand probability ≥ 0.35 | 40%
9 | ECO | Dark road with low expected demand | 20%
05
Notes: Read only the first three states aloud, then summarize the rest.
Brightness increases immediately. Decreases ramp by 15 percentage points no faster than every 500 ms.
Source: src/control_engine.cpp in the project repository.

## Slide 6
Explainable prediction and coordinated light wave
Chart: 
| Recent activity | Historical hour | Adjacent zones | Current PIR
Base demand score | 35 | 30 | 20 | 15
Base weights (%)
A bounded positive-trend bonus reacts to rising traffic.
One PIR event lights the road ahead
Z1
20%
Z2
100%
Z3
65%
Z4
20%
PIR now
PRELIGHT before arrival
The predictor suggests demand. The controller still applies daylight, sensor-health, weather, and emergency constraints.
06
Notes: The weights are implemented in src/predictor.cpp. The score is clamped to 0 through 1.
The historical profile is editable in config/historical_profile.csv.
Emphasize that the predictor recommends demand; the controller enforces safety.

## Slide 7
Failure behavior stays safe and bounded
Sensor invalid or stale
Detected by timestamp, validity, or timed send
70% SENSOR_FAILSAFE
Critical controller loop does not wait forever
Predictor delayed or stopped
Detected by timestamp, validity, or timed send
Rules and live sensors continue
Critical controller loop does not wait forever
Status queue full
Detected by timestamp, validity, or timed send
One display frame is dropped
Critical controller loop does not wait forever
Emergency path
A separate service and priority-31 event bypass prediction and immediately set all targets to 100%.
07
Notes: Use this slide for the reliability score in the rubric.
Each queue send has a timeout. Status loss affects presentation only, not control.
Source: src/main.cpp and src/control_engine.cpp.

## Slide 8
Mandatory CLI and live fault injection
$ ./lumigrid --interactive
lgrt> occupancy 2 3
lgrt> emergency on 5
lgrt> status
Zone Lux PIR Predict Bright Mode
1 18 no 31% 65% PRELIGHT
2 17 YES 68% 100% ACTIVE
3 19 no 28% 65% PRELIGHT
4 18 no 22% 20% ECO
Emergency=ON every target=100%
Judge actions
occupancy 2 3
Moving light wave
emergency on 5
Timed priority override
fault 3 on
Sensor fail-safe
lux 500
Daylight control
auto
Clear injected inputs
08
Notes: Let a judge choose one command. The CLI is the required interface, not a prerecorded animation.
The displayed values illustrate the implemented modes; live numbers vary with timing and scenario.
Run command: make interactive.

## Slide 9
Host baseline: safety demand determines the saving
September 12, 2026; four processes; 100 ms scenario sampling
Chart: 
| Daylight | Quiet night | Sensor fault | Rush hour
Estimated saving | 79.998 | 73.17 | 34.94 | 11.571
Estimated energy saving (%)
Eight-zone stress run
3,331
messages in 10.35 s
0
sampling deadline misses
≤ 100 μs
p95 event-latency bucket
71.866 μs
worst emergency latency
Host reference only. QNX Pi measurements replace these before final submission.
09
Notes: Do not call these QNX results. They are Linux host validation from docs/TEST_REPORT.md.
Energy is integrated from commanded brightness against a 100%-brightness baseline. It is not a wattmeter reading.
Source data: run matrix and stress summary.json files generated September 12, 2026.

## Slide 10
Raspberry Pi and QNX target integration
The controller and predictor stay unchanged when simulated inputs become hardware inputs
Inputs
LDR through ADC
PIR occupancy
Emergency button
Raspberry Pi
QNX OS 8.0
POSIX message queues
FIFO priorities
Outputs
PCA9685 PWM
Four LED zones
Serial and CSV evidence
Tuesday bring-up sequence
1
Boot the exact Pi BSP and run hello world
2
Run LumiGrid-RT in simulator mode on the QNX target
3
Verify GPIO, I2C or SPI interfaces one device at a time
4
Capture QNX CPU, memory, priority and latency evidence
Working QNX simulation remains the honest fallback if a sensor driver fails.
10
Notes: The Pi has no analog input, so the LDR needs an ADC such as ADS1115 or MCP3008.
Confirm the exact Pi model, BSP, and driver interfaces before writing a hardware adapter.
QNX SDP documentation: https://www.qnx.com/developers/docs/8.0/
The official deck checklist supplied by the team requires Software Center, Momentics, BSP, libraries, and tested hardware readiness.